## Slide 1: Binary Shifts
A shift involves moving the bits stored in a register a given number of places within the register.
Each bit within the register may be used for a different purpose.
Example in the IR each bit identifies a different interrupt.

## Slide 2: Binary Shifts
Types of shifts
Logical
Arithmetic
Cyclic Shifts

## Slide 3: video

## Slide 4: Logical & Arithmetic Left Shift
Each bit is moved one left
The most significant bit(left most) is discarded
A zero is added to the right
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Logical
Arithmetic

## Slide 5: Logical & Arithmetic Left Shift
Each bit is moved one left
The most significant bit(left most) is discarded
A zero is added to the right
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Logical
Arithmetic

## Slide 6: Logical & Arithmetic Left Shift
Each bit is moved one left
The most significant bit(left most) is discarded
A zero is added to the right
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 
Logical
Arithmetic

## Slide 7: Logical & Arithmetic Left Shift
Each bit is moved one left
The most significant bit(left most) is discarded
A zero is added to the right
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 
Logical
Arithmetic

## Slide 8: Logical & Arithmetic Left Shift
Each bit is moved one left
The most significant bit(left most) is discarded
A zero is added to the right
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
Logical
Arithmetic

## Slide 9: Logical & Arithmetic Left Shift
Each bit is moved one left
The most significant bit(left most) is discarded
A zero is added to the right
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
Logical
Arithmetic

## Slide 10: Logical / Arithmetic Left Shift Examples
10110101 | 01011010
<< 2 | << 4

## Slide 11: Logical / Arithmetic Left Shift Examples
10110101 | 01011010
<< 2 | << 4
11010100 | 10100000

## Slide 12: Logical Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
A zero is added to the left
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Logical

## Slide 13: Logical Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
A zero is added to the left
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Logical

## Slide 14: Logical Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
A zero is added to the left
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Logical

## Slide 15: Logical Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
A zero is added to the left
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Logical

## Slide 16: Logical Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
A zero is added to the left
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Logical

## Slide 17: Logical Right Shift Examples
10110101 | 01011010
>> 3 | >> 5

## Slide 18: Logical Right Shift Examples
10110101 | 01011010
>> 3 | >> 5
00011010 | 00000010

## Slide 19: Arithmetic Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
The most significant bit is copied to the left hand side
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Arithmetic

## Slide 20: Arithmetic Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
The most significant bit is copied to the left hand side
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Arithmetic

## Slide 21: Arithmetic Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
The most significant bit is copied to the left hand side
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Arithmetic

## Slide 22: Arithmetic Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
The most significant bit is copied to the left hand side
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Arithmetic

## Slide 23: Arithmetic Right Shift
Each bit is moved one right
The least significant bit(right most) is discarded
The most significant bit is copied to the left hand side
repeat for the number of shifts required...
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Arithmetic

## Slide 24: Arithmetic Right Shift Examples
10110101 | 01011010
>> 2 | >> 4

## Slide 25: Arithmetic Right Shift Examples
10110101 | 01011010
>> 2 | >> 4
11101101 | 00000101

## Slide 26: Cyclic Shift (Left / Right)
Each bit is moved along (left or right)
The bit that drops off the end is moved to the other end
No bits are lost
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Cyclic

## Slide 27: Cyclic Shift (Left / Right)
Each bit is moved along (left or right)
The bit that drops off the end is moved to the other end
No bits are lost
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Cyclic

## Slide 28: Cyclic Shift (Left / Right)
Each bit is moved along (left or right)
The bit that drops off the end is moved to the other end
No bits are lost
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Cyclic

## Slide 29: Cyclic Shift (Left / Right)
Each bit is moved along (left or right)
The bit that drops off the end is moved to the other end
No bits are lost
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Cyclic

## Slide 30: Cyclic Shift (Left / Right)
Each bit is moved along (left or right)
The bit that drops off the end is moved to the other end
No bits are lost
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Cyclic

## Slide 31: Cyclic Shift Examples
10110101 | 01011010
>> 2 | << 4

## Slide 32: Cyclic Shift Examples
10110101 | 01011010
>> 2 | << 4
01101101 | 10100101

## Slide 33: Summary
Logical left
Arithmetic left
Move all bits to the left MSB is discarded Zero is add to the right | Preserves the sign bit Move all bits to the right LSB is discarded MSB is copied to the left | Move all bits along The bit that falls off one end is added back to the other end
Arithmetic right
Cyclic